## Slide 1: Introduction to Pulse Width Modulation (PWM)
Kai Huang, Gang Chen, Hardik Shah, Biao Hu

## Slide 2: Wheel ECU
  Encoder available only on the handmade car
  For LEGO cars, one Neno board for all wheels
  Handmade car has one Neno board per wheel
  LEGO -> iMX6 as a central ECU
  Handmade -> DE2-115 as a central ECU
Motor
Wheel
Nano board
H-Bridge
Encoder
Central ECU

## Slide 3: What is an FPGA ?
FPGA – “Field Programmable Gate Array”
What FPGA can do:
  Can you use your Intel processor as an AMD processor tomorrow and again as an Intel processor the day after tomorrow?
  You receive software updates frequently, did you ever received a hardware update? Can you upgrade your core i5 to core i7?
  Can you fix a bug in your chip after you have already received it?
Notes: Ask these questions to the audience to make it interactive and keep them along.

## Slide 4: What is an FPGA ?
FPGA is a “Programmable Hardware”
  As you do software programming to get the desired functionality, FPGA must be programmed to get the desired functionality.
  At power-on FPGA is blank and cannot perform any task. It must be programmed to use as a particular hardware.
  Due to the “programmable” feature, the FPGA is highly flexible and upgradable.

## Slide 5: Two main Companies
We chose Altera for this lab course

## Slide 6: FPGA usage flow
Power On
Program the device
Use the device
Power Off
Programming is Lost
Programming using configuration file
Use the device as a processor, a memory, a DSP etc

## Slide 7: FPGA programming flow
Power On
Program the device
Use the device
Power Off
Programming is Lost
Programming using configuration file
Use the device as a processor, a memory, a DSP etc

## Slide 8: Altera FPGA programming flow
The Quartus tool takes your design as an input and generates configuration files “.sof” (SRAM Object File) and SOPCINFO (more on it later) files
Quartus Tool
Configuration file:
.sof and SOPCINFO file

## Slide 9: FPGA usage flow
Power On
Program the device
Use the device
Power Off
Programming is Lost
Programming using configuration file
Use the device as a processor, a memory, a DSP etc
The main focus of this Lab

## Slide 10: Flow used in this lab course
You need to install web edition of Quartus tool from Altera website
Nios II
Memory
JTAG Uart
Quartus Tool
.elf
.sopcinfo
Nios II SBT for Eclipse
.c & .h files
Your tasks
.sof

## Slide 11: Save images on the board
Convenient use
  HW (.sof) and SW (.elf) image will be loaded at power-on from the FLASH memory
Store images here

## Slide 12: Questions

## Slide 13: What is PWM
Output signal alternates between on and off within specified period
Only the duration of “on time” and “off time” varies

## Slide 14: What is PWM?
Depending on the requirement the width of the pulse is modulated (adjusted).
Duty cycle = ton / (ton + toff).
on off
on off
Duty cycle = 20%
Duty cycle = 50%
Width
period

## Slide 15: Why PWM?
Maximum voltage
100 %
50 %
75 %
Analog voltage control:
  Voltage can be changed to control the motor speed
  Can NIOS change voltage ?
t

## Slide 16: Why PWM?
50 %
Digital voltage control:
  Can only control ‘1’ and ‘0’
  X% of maximum analog voltage = X% of duty cycle
t
t
1
0
Analog control
Digital control
=

## Slide 17: Usage of PWM
Motor Control
Intensity of LED

## Slide 18: How to generate PWM signal ?
Software method
  Using counter
    Count to 100 in a loop
    Set the output value to 1 in the beginning of the loop
    Set the output value to 0 as soon as the counter reaches the value of required duty cycle.
    Continue the process
  Using interrupt
    Home work
    Think about the concept

## Slide 19: Hardware PWM IP
Programmable/configurable
Precise
A good obedient, the boss can RELAX !!!
NIOS core
RAM
JTAG Uart
Your PC
USB Blaster
PWM

## Slide 20: Hardware PWM IP
Follow the simple use sequence
  Enable, Configure, Modify, Disable
Only one function for controlling two PWM signals
motor_setting(duty1, duty2, period, enable);
Two PWM signals are required to drive a single motor
  One for each direction

## Slide 21: Questions

## Slide 22: H-Bridge: How does a motor turn?
If you want to change the direction of the rotation, change the direction of current flow
5 V
gnd
i
gnd
5 V
i

## Slide 23: How much current does a motor need?
Your nano board works @ 5 V, 0.5 Ams AT MOST
Depending on the application, motors need huge amount of voltage and current

## Slide 24: How much current does a motor need?
Can I connect my Nano board to 25K Volts?
Yes you can
  Please inform me before doing it, I will run away from you as far as possible
You should use electric switch
  Relay
  Transistor/h-Bridge

## Slide 25: Relay : Electro mechanical switch
The small current flowing from coil creates electro-magnetic force which attracts the pivoted contact and circuit is closed on the large current side
  Provides isolation
  Slow reaction due to mechanical motion
small current
large current
gnd
25k V

## Slide 26: H-Bridge
Drive signal A & B from your Nano board
  Transistor is an electronic switch
  What happens if A = 1, B = 1 and V = 25 K?

## Slide 27: H-Bridge
A & B must be driven by square wave pulses as shown above

## Slide 28: Component: H-bridge Circuit
L298 chip & Circuit

## Slide 29: Goals
Forward
Backward
Rotate clockwise
Rotate anticlockwise

## Slide 30: Questions